## Slide 1: The Cog Project: Building a Humanoid Robot
Rodney A. Brooks, Cynthia Breazeal, Matthew Marjanovic, Brian Scassellati, Matthew M. Williamson
Presented by Edward Venator

## Slide 2: Introduction
Cog: a Humanoid Robot
Two goals
  Build a general purpose humanoid robot
  Gain understanding of human cognition
Uncovered new problems and solutions in control theory, robotics, and AI.
Draws on many social science fields

## Slide 3: Methodology

## Slide 4: Methodology
Classical AI
Monolithic internal models
Monolithic control software
General purpose processing
Not biologically plausible
Computationally intensive
New Methods
Inspired by cognitive science
Four attributes
  Developmental organization
  Social interaction
  Embodiment/physical coupling
  Multimodal integration

## Slide 5: False Assumptions in Classical AI
Monolithic internal models
  Humans do not notice minor changes in a scene, only major changes
  Humans do not store a full world model
Monolithic control
  Humans with surgically split brains maintain separate but complementary control systems
  Humans have multiple, independent control systems
General purpose
  There are tasks that humans are good at, and computationally similar tasks that humans are bad at
  Humans are more emotional than rational

## Slide 6: Human Intelligence: Four Aspects
Development
  Build skills incrementally
  Reduces the difficulty of learning
  Systems that scale autonomously
Social Interaction
  Allows for human-machine interaction
  Facilitates learning
Embodiment
  Real (humanoid) systems are necessary for human intelligence
  Offloads calculation of most physical dynamics to the real world, rather than simulating it (gravity, friction, etc)
  Allows exploitation of system dynamics
Integration
  Senses are not independent
  One sense can benefit from information from another (e.g. Moving things make noise, allowing interaction between visual and auditory systems

## Slide 7: Computation Hardware
“Brain” made of several networked processor nodes
Digital signal processors to handle visual/auditory sensor data
Each joint controlled by its own small microcontroller, which reads joint sensors and controls joint motor

## Slide 8: Perception Hardware
Visual
  Two articulated eyes
  Each eye has a high resolution, low field-of-view camera and a low resolution, high field-of-view camera
Vestibular
  Analogous to human inner ear
  Gyroscopic yaw rate sensors and accelerometers
Auditory
  Two ears with onmnidirectional microphones
Tactile
  Array of pressure sensors on the robot’s torso
  Pressure sensors on some hands
Kinesthetic
  Incremental encoders on all joints
  Temperature and current sensors (crude force sensing) and limit sensors on all joints except eyes
  Strain gauges, absolute position sensors, and limit switches on arms

## Slide 9: Motor Hardware
Arms
  6 DOF, human proportions
  Series elastic actuators
  Virtual spring damper system; moved by changing equilibrium position
3 DOF Neck
2 DOF Torso
1 DOF Spine Twist

## Slide 10: Development Hardware
Emotive Response Platform (Kismet)
  Facial features (eyelids, eyebrows, mouth)
  Able to show 9 expressions linked to “emotions”
Vision Platform
  Color Cameras
Vision-auditory platform
  Simplified vision system

## Slide 11: Long-Term Projects

## Slide 12: Joint Attention
Definition: The recognition of others as agents with their own beliefs, desires, and perceptions
Necessary for social interaction
Necessary for learning using normal social interaction
Requires coordination of many systems and processes

## Slide 13: Infant/Caretaker Social Interaction
Two-way interaction with a caretaker
  Caretaker interacts with infant/robot
  Infant/robot responds emotionally
  Caretaker modifies behavior as a result of infant/robot’s reaction
Should be possible for robot to learn how to influence caretaker with emotional responses

## Slide 14: Dynamic Arm Motion
Kinematic solutions to joint position/force are computationally expensive
Instead, exploit mechanical characteristics of the robot’s body
Independent controllers at each joint, couple through the physical body of the robot
Robust to perturbation, no need for accurate calibration, computationally simple

## Slide 15: Multi-Modal Coordination
Need a facility for combining skills
  Combine sensory inputs
  Synergistic interaction of motor systems
  “Sensory tuning” i.e. a motor system is used to increase the effectiveness of a sensory system
Requires performance measures of sensorimotor systems (sensory confidence measures, motor accuracy and effort measures). These are easy to determine.
Requires segmentation of data stream into “events” to allow correlation of events. This is hard to do.

## Slide 16: Current Tasks

## Slide 17: Visual-Motor Routines
Saccades
  Quick motion to center an object in the visual area
  Saccade function maps target and eye position to change in eye position.
  Target position is determined by computer vision. Eye position is measured from encoders.
  Saccade function created by unsupervised learning
Smooth-Pursuit Tracking
  Keeps moving object centered in visual area
  Uses computer vision to determine object speed.
  Moves eyes to match
Binocular Vergence (point both eyes at the same target)
Vestibular-ocular Reflex (VOR) and Opto-kinetic Reflex (OKN)
  VOR stabilizes the eye during rapid head movement using the vestibular system, but is prone to drift over time
  OKN stabilizes the eye during slow head movement using optical flow, and can be used to train VOR gains and cancel VOR drift

## Slide 18: Eye-Neck Orientation
Animals turn their heads to center their eyes, which maximizes the range of subsequent eye motions
Requires a mapping from neck and eye position onto change in neck position. This is a linear mapping.
Using VOR to counter-rotate eyes during neck motion can result in instability due to vibration.
In order to keep the eyes stable during neck motion, counter-rotate them with the same (scaled) velocity commands as the neck.

## Slide 19: Dynamic Oscillator Motor Control
Joint positions can be modeled by the control law
The arm is moved by moving equilibrium points
A neural network oscillator can be used as a controller
  yout added to a fixed equilibrium point to determine the equilibrium point
  Any number of sensor positions can be inputs gj
Oscillator dynamics coupled to physical dynamics of system
Can entrain to an input signal over a wide range of frequencies, typically within one cycle.

## Slide 20: Pointing to a Visual Target
The robot must point with its arm at a target in its vision.
The robot first saccades to the target and uses eye position to parameterize the target location.
The robot must have a mapping from eye position to joint positions. This mapping is learned incrementally as the robot attempts to point at targets.

## Slide 21: Other Tasks
Recognizing joint attention through face and eye finding
Imitating head nods
Regulating interaction through expressive feedback

## Slide 22: Future Research Directions
Coherence
  Currently different behaviors operate independently
  Behaviors assume total control over the system
  Behaviors cannot coexist
Other perceptual systems
  More use of kinesthetic and force sensing
  Chemical senses (not practical with sensor technology)
Deeper visual perception
  Object and facial recognition
  Should be simple and learned
Sense of Time